## Slide 1
AMD ON WHEELS NZ · 2026 · WORKSHOP
Agentic AI for HLS:
a synthesizer on Kria
You'll hear a 16-voice synth run on a KV260, then we go through how it got built with Ross and Vitis HLS, and what you can repeat yourself.
David Farrell, Field Application Engineer, Avnet
Notes: TIMING: 0:00-0:45 (workshop is 30 min total; plan below adds to about 30).
Say what the room will get: sound first, then how it was built. Keep the intro short, don't read the slide.
DEMO: have the KV260 powered, FC25 plugged in, and the bench audio on before the slide comes up.
NOTE: title is still the working one. Final public title is not locked.

## Slide 2
FINISHED DEMO
Here it is working first, then we look at how
AMD on Wheels NZ · together we advance_
2
LIVE DEMO
(drop backup recording in this frame)
What you should hear
Notes from the FC25 coming out of the Pmod DAC, chords up to ten notes, four controls that change the sound.
What to look for
Terminal showing the board is alive: identity register reads SYNT and the overrun count stays at 0.
VERIFY
Notes: TIMING: 0:45-3:30.
LIVE: play single notes, then a chord, then turn the four knobs (CC 93, 91, 71, 74). Let people hear it for a bit before talking.
BACKUP: if no sound within about 15 seconds, say 'let me switch to the recording' and play the backup clip (embed it on this slide, or open it from the take-home folder). Don't debug live.
RESUME: after either path say 'so that is what we're going to be taking apart' and move on.
Success condition (visible): audible notes, and the regread terminal showing overrun count 0.

## Slide 3
HOW IT WORKS
A MIDI key press turns into audio in about five steps
AMD on Wheels NZ · together we advance_
3
HUMAN
FC25 keyboard
MIDI over USB
PLATFORM
Linux + ALSA
C process, 3 ms loop, keeps voice + knob state
PLATFORM
AXI registers
shadow copy, then one commit
TOOL
HLS synth (PL)
one sample per call, 16 voices
PLATFORM
Pmod I2S2 DAC
24-bit audio, speakers
input -> processing -> output
Processing is split: Linux does the slow stuff (notes, knobs), programmable logic does the fast stuff (the actual sound).
Notes: TIMING: 3:30-5:30.
Walk the diagram left to right once. Linux side first (ALSA -> C process), then the PL side (registers -> HLS -> I2S).
Point: Linux never makes audio samples. It only keeps the state (which voices, which knob values). The PL makes one sample at a time at 48 kHz.
Detail if asked: control loop runs every 3 ms; register page is 4 KiB; 'commit' register publishes a whole snapshot at once so the DSP never sees half an update.

## Slide 4
WHY IT IS HARD
Three things make this harder than it looks
AMD on Wheels NZ · together we advance_
4
Real time
48,000 samples a second, and each one needs a full 16-voice calculation plus reverb. One HLS call has to finish inside 2,000 cycles at 100 MHz. It takes 1,803 worst case, so not much slack.
Linux meets FPGA
Software changes notes and knobs whenever it likes, the logic wants a steady picture. We need a copy-then-commit scheme so a sample never sees half an update.
Fitting and timing
Nearly full: about 81k of 117k LUTs and 398 of 1,248 DSPs. And audio data has to cross into its own clock domain without glitching.
Notes: TIMING: 5:30-8:00.
Keep to three. 1) real-time: a new audio sample is needed every ~20.8 microseconds. 2) it is Linux AND FPGA together, so state has to cross between them safely. 3) it has to fit: it's a big design on the K26.
Also mention the audio clock is different from the main PL clock, so audio samples cross a clock boundary (CDC). Don't go deep unless someone asks.

## Slide 5
WORKSHOP TARGET
What you should be able to do by the end
AMD on Wheels NZ · together we advance_
5
You can repeat
Write a short spec for a DSP block, get Ross to produce Vitis HLS for it, run C simulation and the HLS reports, and decide yourself if the result is good enough.
How you know it worked
C sim passes, co-sim passes, the HLS report meets the timing and cycle target, and in the full design the routed timing is met and you can hear the sound.
VERIFY
Notes: TIMING: 8:00-9:30.
Be honest about scope: the synth itself is frozen and finished. What attendees reproduce is the METHOD (short spec, instruct Ross, inspect, build, test, revise), applied to a piece of the design. Take-home pack has the full spec, prompts and setup.

## Slide 6
PLATFORM COMPARISON
Only a few AMD options were really in the running
AMD on Wheels NZ · together we advance_
6
Criterion | Kria K26 (KV260 kit) | Kria K24 (KD240 kit) | Kria AI SOM
Programmable logic | Large, MPSoC with fabric | Smaller fabric (check) | Not what it is for
Runs Linux + ARM cores | Yes | Yes | Yes (x86)
Easy audio output | Pmod header on the kit | Different kit I/O | Different kit I/O
Dev support | Starter kit, EDF/Ubuntu, Vivado + Vitis | Starter kit, same tools | New, still ramping
Fits this design | Yes (81k LUTs used) | Needs checking | No fabric to fit it in
Notes: TIMING: 9:30-11:00. One slide only, don't linger.
The KV260 is the starter kit for the K26 SOM. Numbers for K24 / Kria AI SOM are deliberately not on the slide: VERIFY official specs and names before release, as per Joe's spec.
Short version: needed a big programmable fabric, Linux, and a Pmod header for the DAC. K24 is smaller, and the AI SOM is a different kind of device (CPU/GPU/NPU, no PL fabric for this).

## Slide 7
PLATFORM DECISION
KV260 it is: enough fabric, Linux, and a header for the DAC
AMD on Wheels NZ · together we advance_
7
PLATFORM
Why K26 / KV260
- Fabric big enough for 4 HLS voice lanes plus reverb - Arm cores run Linux and the MIDI/control process - Pmod header J2 takes an I2S DAC with no extra board - Starter kit and documented tools, so it is reproducible
Trade-offs
- Uses most of the device (about 14.2k of 14.6k CLBs occupied) - Timing is tight-ish: setup slack +0.828 ns, hold +0.010 ns - Audio clock about +19.3 ppm off, we accepted that - Not low power-optimised, that was not the goal
Notes: TIMING: 11:00-12:30.
Trade-offs to say out loud: the K26 is more than a synth strictly needs, we use most of it though. Audio clock comes out at about +19.3 ppm off ideal, accepted, doesn't matter for this demo. Pmod I2S2 is a cheap DAC, not studio quality.
Don't claim it's the only possible choice.

## Slide 8
TOOLCHAIN
Each tool has one job in the flow
AMD on Wheels NZ · together we advance_
8
TOOL
Vitis HLS
C++ DSP to logic. C sim, synthesis, co-sim, estimates.
TOOL
Vivado
Block design, build, routed timing and utilisation, bitstream.
PLATFORM
Ubuntu, then EDF
Developed on AMD Ubuntu 24.04. EDF 25.11 later packaged the accepted build.
ROSS
Ross
Drives the tools, writes and edits sources, reads reports.
Notes: TIMING: 12:30-14:00.
Vivado = the full design (block design, synthesis, place and route, timing reports, bitstream). Vitis HLS = turns the C++ DSP into logic and gives cycle/timing estimates. Ross = sits in the middle and operates the tools and edits files when asked. Linux/EDF = the runtime.
Be clear that HLS numbers are estimates and routed Vivado numbers are the real ones.

## Slide 9
ROSS AND HUMAN REVIEW
Ross does the legwork, the engineer decides what counts
AMD on Wheels NZ · together we advance_
9
ROSS
Ross can help with
- Exploring options and reading reports - Writing and editing the HLS and control code - Running the tools and reading back results - Working out why something failed
HUMAN
The engineer still checks
- The spec and the acceptance boundary - Source changes, constraints, clock crossings - Reports, timing, and test results - Register readback and the actual audio
Ross does not replace the engineering judgement. You pick the product, the trade-offs, and what is good enough.
Notes: TIMING: 14:00-16:00.
Use Ross's official wording once: 'AMD Ross spans software, silicon, and board design to dramatically accelerate embedded system design, optimization, debug, and deployment compared to typical development lifecycles. Unlike generic AI assistants, AMD Ross is built around AMD Embedded development environments, institutional AMD engineering knowledge, and expert-authored methodologies.' (AMD launch copy, 30 Sep 2026.)
Don't turn that into numbers. We have no measured speed-up to claim, so don't.

## Slide 10
SPEC-DRIVEN WORKFLOW
One loop, repeated: spec, build, test, feedback, revise
AMD on Wheels NZ · together we advance_
10
HUMAN
Short spec
ROSS
Instruct Ross
ROSS
Code changes
HUMAN
Human review
VERIFY
Build + test
HUMAN
Feedback
revise and go round again
Notes: TIMING: 16:00-18:00.
One diagram only. The full multi-stage version (brainstorm, spec, plan, task, review) is in the take-home pack, not here.
Say: the spec is the thing that stays still; the code is what changes.

## Slide 11
GUIDED STEP
One real step: ask Ross for speed only and see
AMD on Wheels NZ · together we advance_
11
HUMAN
The instruction
"Optimise for Fmax only." That was the whole brief. Nothing about cycles, area, or how.
ROSS
What Ross did
Split the running sum into four partial sums, then a two-level combine.
VERIFY
HLS estimate, core only
Before: 114 cycles at 13.301 ns After: 136 cycles at 7.230 ns (target was 10 ns)
Cycles went up a bit, clock period got much shorter. That was what the brief asked for, so fine.
One other idea (reciprocal multiply) saved LUTs but did not help the clock, so we dropped it.
Notes: TIMING: 18:00-23:00. This is the main live/guided part.
CUE: show the instruction text on screen, then the result. If the live HLS run is too slow, use the PREBUILT CHECKPOINT (reports from the saved run) and say so.
BACKUP: recording of the HLS run in the take-home folder; switch with 'this takes a few minutes, here's one I made earlier'.
RESUME: land on the numbers table, then go to verification.
CLAIMS: these numbers are for the single focused core, from HLS ESTIMATES, not the whole design. Whole accepted builds are about 1,800 cycles. Say that.

## Slide 12
VERIFICATION
Reports are one thing, the board has to agree
AMD on Wheels NZ · together we advance_
12
VERIFY
Routed in Vivado
80,882 / 117,120 LUTs 398 / 1,248 DSP48E2 15 / 144 Block RAM Setup slack +0.828 ns Hold slack +0.010 ns
VERIFY
On the board
Register 0xA0000000 reads 0x53594e54 (SYNT), ABI 0x00010000. FC25 run: 394 events captured, all four knob values matched the PL shadows, zero overruns.
HUMAN
To the ears
Notes, velocity, knobs, four and ten note chords, releases. And a human listening, which is the check no report does for you.
Notes: TIMING: 23:00-26:00.
Separate the layers: HLS estimate vs routed Vivado vs hardware. The routed numbers are the ones that count.
Optionally run 'regread 0xA0000000' live and show 0x53594e54 (SYNT).
Don't say EDF built the FPGA design. It didn't; Vivado/Vitis 2025.2 did, EDF just packaged and boots it.

## Slide 13
RECAP
Result, platform, tools, way of working
AMD on Wheels NZ · together we advance_
13
VERIFY
Result
A working 16-voice synth on a KV260
PLATFORM
Platform
Kria K26: fabric + Linux + Pmod
TOOL
Tools
Vitis HLS, Vivado, Ross
HUMAN
Way of working
Short spec, instruct, review, test, revise
Same method should work on your own DSP block, it just needs a clear spec and a way to check the answer.
Notes: TIMING: 26:00-28:00. Read the four boxes quickly. One more time: Ross assists, the engineer decides. No time-saving claim made, because we have not measured a fair baseline.

## Slide 14
CONTINUE AFTERWARDS
Everything you need to try it is in the take-home pack
AMD on Wheels NZ · together we advance_
14
Take-home pack
Full spec, the prompts used, setup steps, and how to verify. (link / QR to be added)
QR here
ROSS
AMD Ross
amd.com/en/products/software/ross-agentic-ai.html github.com/xilinx/ross-ai-assistant The synth stays at the bench, come and play it.
Notes: TIMING: 28:00-30:00.
TODO BEFORE RELEASE: add real QR codes and URLs for the take-home pack (full spec, prompts, setup, verification steps). Ross links below come from AMD's launch announcement.
Invite questions; the frozen prototype stays playable at the bench afterwards.